## Slide 1: Arduino gyroscope/accelerometer sense axes
Y
X
Z

## Slide 2: Basic Orientation Sensing (Tends to be noisy or drifts)
Gyro Data (XYZ)
Angular Rate
x
New Attitude Est (3x3)
Previous Attitude Est (3x3)
Convert to DCM
(3x3)
Accelerometer Data
Convert to Euler Angles (Ψ,Θ, Φ), optional
Is total acceleration magnitude ~1G?
roll (Ψ)= atan2(ay, az)
pitch(Θ) = -sin(ax)
YES
No
No valid measurement
Tends to drift, integrates bias in gyroscope
Tends to be noisy and not always valid due to actual acceleration. Only measures two orientation axes.
Delay

## Slide 3: Adaptive Data flow block Diagram
Gyro Data (XYZ)
Angular Rate
x
[0
0
9.81]
New Attitude Est (3x3)
Current Attitude Est (3x3)
Convert to DCM
(3x3)
x
Gravity @Local level
Accelerometer Output Estimate (assuming stationary) (3x1)
Accelerometer Data
Adaptive filter
Σ
+
-
Combine these in some way
Previous Attitude Est (3x3)
Delay

## Slide 4: Another Possible Approach
Gyro Data (XYZ)
Angular Rate
x
New Attitude Est (3x3)
Current Attitude Est (3x3)
Convert to DCM
(3x3)
Accelerometer Data
Convert to Euler Angles (Ψ,Θ, Φ)
Is total acceleration magnitude ~1G?
roll (Ψ)= atan2(ay, az)
pitch(Θ) = -sin(ax)
YES
No
No valid measurement
Ψ
Θ
Ψ
Θ
Adaptive Filter
Σ
Σ
+
-
+
-
εΨ, εΘ
εΨ, εΘ

## Slide 5: Geometric Update equations
Find DCM update equation based on gyroscope output
[constants: R2D = pi/180. dt = 1/fs]
gx, gy, gz = gyroscope x/y/z “Delta Theta” (angular rate * dt)
imu_dcm_x = [...
1, 0, 0;
0, cos(gx), -sin(gx);
0, sin(gx), cos(gx)];
imu_dcm_z = [...
cos(gz), -sin(gz), 0;
sin(gz), cos(gz), 0;
0, 0, 1];
imu_dcm_y = [...
cos(gy), 0, sin(gy);
0, 1, 0;
-sin(gy), 0, cos(gy)];
Transition_dcm = (imu_dcm_x * imu_dcm_y * imu_dcm_z)’;
Find Euler angles based on DCM;
current_attitude_dcm(j,:,:) = temp_attitude;
current_attitude_euler(j,1) = [atan2( DCM_BI(2,3), DCM_BI(3,3))]; %roll
current_attitude_euler(j,2) = [asin(DCM_BI(1,3))]; %pitch
current_attitude_euler(j,3) = [atan2(DCM_BI(1,2), DCM_BI(1,1))];%yaw
Find Euler angles based on accelerometer reading (a tilt sensor, essentially)
Assumes no acceleration (if magnitude of acceleration is ~1G then this is probably true)
Accelerometer outputs: ax, ay, az (normalized in “G’s”, or divided by 9.81)
Roll = atan2(ay,az);
Pitch = -asin(ax);